## Slide 1: Computer Networks
CS 430

## Slide 2: Network Layer

## Slide 3: Objectives
Forwarding and Routing
Internet Protocol
  IPv4
  IPv6
  ICMP
Routing algorithms
  link state
  distance vector
  hierarchical routing
  BGP

## Slide 4: Network Layer
Host-to-host
Sender encapsulates segments into packets
Receiver extracts segments to transport layer
Network layer protocols in every host, router
Router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 5: Network Layer Functions
Forwarding
  Move packets within a router
Routing
  Determine a route taken by packets from source to destination
  Routing algorithms

## Slide 6: Network Layer Planes
Data Plane
Local, per-router function
Determines how datagram arriving on router input port is forwarded to router output port
Forwarding function
Control Plane
Network-wide logic
Determines how datagram is routed among routers along end-end path from source host to destination host
Two control-plane approaches
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers

## Slide 7: Per-router Control Plane

## Slide 8: Logically Centralized Control Plane

## Slide 9: Connection Setup
What network layer protocol(s) do you know?
  IP, IPv6
There are others too!
  ATM, frame relay, X.25
Virtual connection established
  Like TCP
  Hosts and routers are involved
Circuit switching vs packet switching
  Host-to-host
  Mutually exclusive
  Network core
Internet
  Best effort
  No guarantees
  No congestion control

## Slide 10: Network Service Model
Individual packets
  Guaranteed delivery
  Guaranteed delay
Packet flow
  In-order delivery
  Guaranteed minimum bandwidth
  Max jitter
  Security

## Slide 11: Packet (Datagram) Networks
No call setup at network layer
Routers: no state about end-to-end connections
  no network-level concept of “connection”
Packets forwarded using destination host address
1. send datagrams
application
transport
network
data link
physical
application
transport
network
data link
physical
2. receive datagrams

## Slide 12: Routers

## Slide 13: Packet Forwarding

## Slide 14: Packet Forwarding Table

## Slide 15: Longest Prefix Matching
Destination 1
  11001000 00010111 00010110 10100001
Destination 2
  11001000 00010111 00011000 10101010

## Slide 16: Router Architecture Overview

## Slide 17: Input Port Functions

## Slide 18: Switching Fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 19: Switching via Memory
First generation routers
  traditional computers with switching under direct control of CPU
  packet copied to system’s memory
  speed limited by memory bandwidth
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 20: Switching via a Bus
Shared bus
Bus contention
  switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers

## Slide 21: Switching via Interconnection Network
Overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
Advanced design
  fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar

## Slide 22: Output Ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission

## Slide 23: Output Port Queuing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!

## Slide 24: How Much Buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT C
.
N

## Slide 25: Input Port Queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 26: Thank You!