## Slide 1: Computer Networks
CS 430

## Slide 2: Transport Layer

## Slide 3: Objectives
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control

## Slide 4: Transport Services
Logical communication between applications
End system protocol
TCP vs UDP
Application layer
  Messages
Transport layer
  TCP segments
  UDP datagrams
Network layer
  Packets
Link-local
  Frames

## Slide 5: Transport vs. Network Layer
Transport layer
Network layer
Protocol(s)
  TCP, UDP
Communication between
  Processes
Identifier used
  Port
Reliability
  Possible
Protocol(s)
  IP, IPv6
Communication between
  Hosts
Identifier used
  IP address
Reliability
  None

## Slide 6: Transport Layer Protocols
TCP
  Congestion control
  Flow control
  Connection setup
UDP
  Best-effort delivery
Unavailable services
  Delay guarantee
  Bandwidth guarantee

## Slide 7: Multiplexing/demultiplexing
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3

## Slide 8: How Demultiplexing Works
Host receives IP packet
  each packet has source IP address, destination IP address
  each packet carries one transport-layer segment
  each segment has source, destination port number
Host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format

## Slide 9: Connectionless Demux: Example
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?

## Slide 10: Connection-oriented demux
TCP socket identified by 4-tuple
  source IP address
  source port number
  dest IP address
  dest port number
demux: receiver uses all four values to direct segment to appropriate socket
server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 11: Connection-oriented Demux: Example
transport
application
physical
link
network
P1
transport
application
physical
link
P4
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets
server: IP address B
threaded server

## Slide 12: User Datagram Protocol

## Slide 13: User Datagram Protocol
RFC 768
Best effort service, UDP segments may be
  lost
  delivered out-of-order to app
Connectionless
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
UDP use
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS, DHCP, NTP, SNMP etc.
Reliable transfer over UDP
  Add reliability at application layer
  Application-specific error recovery!

## Slide 14: UDP: segment header
Why UDP?
No connection establishment (which can add delay)
Simple: no connection state at sender, receiver
Small header size
No congestion control: UDP can blast away as fast as desired
  MGEN
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum

## Slide 15: UDP Checksum
Sender
Receiver
Treat segment contents, including header fields, as sequence of 16-bit integers
Checksum: addition (one’s complement sum) of segment contents
Sender puts checksum value into UDP checksum field
Compute checksum of received segment
Check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless?

## Slide 16: IP Pseudo Header

## Slide 17: UDP Checksum

## Slide 18: UDP Checksum
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Src IP (1) | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Src IP (2) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
SUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Dst IP (1) | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
SUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Dst IP (2) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
SUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Zero+Proto | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
SUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
UDP Length | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
SUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Src Port | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
SUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Dst Port | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
SUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Length | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
SUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Chk Sum | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
SUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DATA (1) | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1
SUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DATA (2) | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
SUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1s COMP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 19: Summary
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP

## Slide 20: Thank You!