## Slide 1: Computer Networks
CS430

## Slide 2: Objectives
Routing protocols
Link state
Distance vector
Intra-AS routing: OSPF
Inter-AS routing: BGP
SDN
SNMP

## Slide 3: Network Layer Functions
Forwarding
  data plane
  move packets from router’s input to appropriate router output
Routing
  control plane
  determine route taken by packets from source to destination
  per-router control
  logically centralized control (software defined networking)

## Slide 4: Per-router Control Plane
Routing
Algorithm
data
plane
control
plane

## Slide 5: Logically Centralized Control
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA

## Slide 6: Routing Protocols

## Slide 7: Overview
Routing protocol goal
  determine “good” paths through network of routers
Path
  sequence of routers from given initial source host to given final destination host
Good path
  least “cost”
  “fastest”
  “least congested”

## Slide 8: A Bit of Graph Theory
Graph
  G = (N,E)
Set of routers
Set of links

## Slide 9: A Bit of Graph Theory
= cost of link
  c(w,z) = 5
cost could always be 1, or inversely related to bandwidth, or inversely related to congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)

## Slide 10: Routing Algorithms
Global vs Decentralized Info
Global
  all routers have complete topology, link cost info
  “link state” algorithms
Decentralized
  router knows physically-connected neighbors, link costs to neighbors
  iterative process of computation, exchange of info with neighbors
  “distance vector” algorithms
Static vs Dynamic
Static
  routes change slowly over time
Dynamic
  routes change more quickly
  periodic update in response to link cost changes

## Slide 11: Link-state Routing Algorithm
Dijkstra’s algorithm
Net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
Computes least cost paths from one node (source) to all other nodes
  gives forwarding table for that node
Iterative: after k iterations, know least cost path to k destinations
  link cost from node x to y
  Start with ∞ if not direct neighbors
  current value of cost of path from source to
  predecessor node along path from source to
  set of nodes whose least cost path definitively known

## Slide 12: Dijkstra’s Algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'

## Slide 13: Dijkstra’s Algorithm
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
uwxvyz

## Slide 14: Dijkstra’s Algorithm
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y

## Slide 15: Dijkstra’s Algorithm
Shortest-path Tree
Forwarding Table
Destination | Link
v | (u,v)
x | (u,x)
y | (u,x)
w | (u,x)
z | (u,x)

## Slide 16: Dijkstra’s Algorithm
Algorithm complexity over nodes
  at each iteration need to check all nodes, , not in
  comparisons
More efficient implementations possible

## Slide 17: Distance Vector Algorithm
Bellman-Ford equation (dynamic programming)
:= cost of least-cost path from x to y
  Min over all neighbors of
  Cost to neighbor
  Cost from neighbor to destination

## Slide 18: Bellman-Ford Example
du(z) = min { c(u,v) + dv(z), c(u,x) + dx(z), c(u,w) + dw(z) }
= min {2 + 5, 1 + 3, 5 + 3} = 4

## Slide 19: Distance Vector Algorithm
= estimate of least cost from x to y
  maintains distance vector
Node x
  knows cost to each neighbor
  maintains its neighbors’ distance vectors. For each neighbor , maintains
Key idea
  from time-to-time, each node sends its own distance vector estimate to neighbors
  when receives new DV estimate from neighbor, it updates its own DV using B-F equation
  under minor, natural conditions, the estimate converge to the actual least cost

## Slide 20: Distance Vector Algorithm
Iterative, asynchronous
Each local iteration caused by
  local link cost change
  DV update message from neighbor
Distributed
  each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
Node process
  wait for (change in local link cost or message from neighbor)
  recompute estimates
  if DV to any destination has changed, notify neighbors

## Slide 21
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 22
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 23: Distance Vector: Link Cost Changes
Link cost changes
  node detects local link cost change
  updates routing info, recalculates DV
  if DV changes, notify neighbors
Good news travel fast
  t0 : y detects link-cost change, updates its DV, informs its neighbors
  t1 : z receives update from y, updates its table, computes new least cost to x , sends its neighbors its DV
  t2 : y receives z’s update, updates its distance table. y’s least costs do not change, so y does not send a message to z

## Slide 24: Distance Vector: Link Cost Changes
Link cost changes
  node detects local link cost change
  bad news travels slow - “count to infinity” problem!
Poisoned reverse
  If routes through to get to :
  tells its (’s) distance to is infinite (so won’t route to via )

## Slide 25: Algorithm Comparison
Message complexity
LS: with nodes, links, messages sent
DV: exchange between neighbors only
  Convergence time varies
Speed of convergence
LS: algorithm requires messages
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
Robustness
  what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
  error propagate thru network

## Slide 26: Routing Protocols

## Slide 27: Hierarchical Routing
Autonomous system (AS)
  A group of routers under the same control
Gateway Protocols
  Interior and Exterior
Routing inside an AS
  Hot-potato routing
  Enhanced Interior Gateway Routing Protocol (EIGRP)
  Routing Information Protocol (RIPv2)
  Open Shortest Path First (OSPF)
  Intermediate System to Intermediate System (IS-IS)
Routing outside an AS
  Policies and metrics
  Border Gateway Protocol (BGP)

## Slide 28: Open Shortest Path First
Open Shortest Path First (RFC 2328)
Broadcasts changes in routing information within AS
Transport layer (Protocol 89)
Optional authentication
  MD5
Multiple paths
Unicast and multicast routing
Hierarchical AS
  Link-state advertisements to all routers in an area
Cost (connection-specific)

## Slide 29: OSPF Hierarchy
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 30: OSPF
An OSPF router forms adjacencies with neighbors
  Hello exchange
  Builds adjacencies database
Dijkstra’s Shortest Path First algorithm to find the best path
Each router sees itself as the central point from which a loop-free, best-cost path to each network is determined

## Slide 31: OSPF Operations
Type | Name | Function
1 | Hello | Neighbor discovery and adjacency maintenance
2 | DB Description | Topological DB summary
3 | LS Request | Request LS info from a neighbor’s DB
4 | LS Update | Advertise available links via network flooding
5 | LS Ack | Response to LS Update

## Slide 32: EIGRP
EIGRP makes use of a composite metric comprised of six different factors
  Hops
  Load
  Bandwidth
  Reliability
  Delay
  MTU
Default formula used for metric calculation in EIGRP

## Slide 33: EIGRP Components
Protocol Dependent Modules
Neighbor discovery and maintenance
  224.0.0.10
  Hello with timeouts
Reliable Transport Protocol
  Cisco’s own layer 4 protocol
  Can provide both reliable and unreliable delivery
Diffusing Update Algorithm (DUAL)
  Quick outage recovery

## Slide 34: Border Gateway Protocol
BGP is a complex protocol
BGP is a very complex protocol
Used to glue together autonomous systems
eBGP
  obtain subnet reachability information from neighboring ASs.
iBGP
  propagate reachability information to all AS-internal routers.
AS determines “good” routes to other networks based on reachability information and policy
Allows advertisement of a subnet existence

## Slide 35: BGP Basics
TCP connection (port 179)
BGP session
  Two peers exchange information about reachable networks
Prefix advertisement means a promise to forward

## Slide 36: BGP Attributes
Autonomous System Number
  Globally unique AS identifier
AS-PATH
  Systems through which prefix advertisement has passed
NEXT-HOP
  Used by routers to configure forwarding tables
Policy-based routing
  Do not route through certain AS

## Slide 37: Route Selection
Local preference
  Policy
Shortest AS-PATH
  DV algorithm
Closest NEXT-HOP
  Smallest least-cost path, as determined by IGP
  Hot-potato touting
Additional criteria

## Slide 38: BGP Routing Policy
X does not want to route from B via X to C
  X will not advertise to B a route to C
Should B advertise path BAW to C?
  It depends

## Slide 39: Why Different Intra-, Inter-AS Routing ?
Policy
  Inter-AS: admin wants control over how its traffic routed, who routes through its net.
  Intra-AS: single admin, so no policy decisions needed
Scale
  hierarchical routing saves table size, reduced update traffic
Performance
  Intra-AS: can focus on performance
  Inter-AS: policy may dominate over performance

## Slide 40: Simple Network Management Protocol

## Slide 41: Network Management
Managed devices
  contain managed objects
Object data is gathered
  Management Information Base (MIB)

## Slide 42: Simple Network Management Protocol
Request/response Mode
Trap Mode

## Slide 43: Simple Network Management Protocol
Message | Function
GetRequest GetNextRequest GetBulkRequest | manager-to-agent: “get me data” (data instance, next data in list, block of data)
InformRequest | manager-to-manager: here’s MIB value
SetRequest | manager-to-agent: set MIB value
Response | Agent-to-manager: value, response to Request
Trap | Agent-to-manager: inform manager of exceptional event

## Slide 44: Generalized Forward and SDN

## Slide 45: Summary
Routing protocols
Link state
Distance vector
Intra-AS routing: OSPF
Inter-AS routing: BGP
SDN
SNMP

## Slide 46: Thank You!